## Slide 1: Surface reconstruction from models for subtractive manufacturing simulation
Bernhard Manfred Gruber
Notes: Welcome,
Next topic is in the area of computational geometry and industrial manufacturing

## Slide 2: Overview
Subtractive manufacturing
Previous work
Problem statement
Approaches
Implementations
Results
Conclusion

## Slide 3: Subtractive manufacturing
http://www.hurco.com/IN/why-hurco/success-stories/blog/PublishingImages/nuconvmx42sr%20cutting.JPG
Notes: Subtractive manufacturing, aka. Machining, is the process of shaping a piece of raw material, usually metal, into a final form.
nitial piece of metal called stock volume.
Each movement of cutting tool, which removes material, is called a sweep.

## Slide 4: Subtractive manufacturing simulation
tool
simplified
tool
swept volume
subtraction
Notes: subtractive manufacturing is simulated using triangle meshes of the stock and cutting tools.
tool is usually approximated by simplified version
tool is repeatedly moved using series of transformations, producing a swept volume with each sweep.
swept volumes are then subtracted from the stock volume

## Slide 5: Previous work – VML
Notes: Foundational to thesis, VML, already implemented most of subtractive manufacturing simulation
Swept volume computation from given tools
Swept volumes can be added to simulate machining process
Custom raycasting algorithm for visualization
Main goals of VML are speed and especially precision

## Slide 6: VML data model
Notes: To maintain precision, VML does not compute Boolean subtractions, but simply stores the SV
Can therefore be seen as maintaining a linearized CSG tree of the stock and a series of SV
To keep triangle count within manageable bounds, a triangle elimination strategy has been developed
Removes triangles which do not contribute to surface of the workpiece
(graphics)
For visualization, the actual surface of the workpiece is sampled by a raycast, which computes the Boolean subtractions on the fly

## Slide 7: Problem statement
Extract triangulated surface from VML data model
Prototypic implementations
Testing on selected scenes
Comparison
  Runtime, memory, complexity, errors, numeric stability, mesh quality, visual quality, feature conservation, …
Notes: However, there are situations where a mesh of the final workpiece is desired, e.g. for verification or physics simulations
This was the goal of my thesis, to extract a triangulated surface …
Several prototypes have been implemented and tested on a few scenes
Compared using various paramteres

## Slide 8: Approaches
Direct intersection of swept volumes
  Most naïve, theoretically most accurate
Point cloud based
  Point cloud easy to create using raycast
  Reconstruction using region-growing on points
  Reconstruction using function fitting
Tri-dexel
  Dexel images easy to create using raycast
  Reconstruction from tri-dexel grid
direct
sampling

## Slide 9: Direct intersection

## Slide 10: Direct intersection
Thomas Möller, A fast triangle-triangle intersection test, 1997
David Rosen, Seamless Intersection Between Triangle Meshes, 2008

## Slide 11: Point cloud based
3 axis-aligned raycasts to sample point cloud

## Slide 12: Ball pivoting algorithm (BPA)
Fausto Bernardini et.al., The ball-pivoting algorithm for surface reconstruction, 1999

## Slide 13: Poisson
isosurface
oriented points
indicator gradient
indicator
Michael Kazhdan etal., Poisson Surface Reconstruction, 2006

## Slide 14: Tri-dexel
http://computingengineering.asmedigitalcollection.asme.org/article.aspx?articleid=1401455
Balázs Tukora, Material removal simulation and cutting force prediction of multi-axis machining processes on general-purpose graphics processing units, 2012

## Slide 15: Tri-dexel
Yongfu Ren et al., Feature conservation and conversion of Tri-dexel volumetric models to polyhedral surface models for product prototyping, 2008
Notes: Based on the 3D grid created by the 3 dexel images, the dexel information can be reorganized into cells

## Slide 16: Tri-dexel

## Slide 17: Test scenes
cylinder_head
impeller
20 SV 80k Δ
2383 SV
6M Δ

## Slide 18: Results – Direct intersection
229ms
149k Δ
21s
1.7M Δ

## Slide 19: Results – Direct intersection

## Slide 20: Results – BPA
0.3 + 4.3s
1.9M Δ
3.8 + 3.7s
1.5M Δ

## Slide 21: Results – BPA

## Slide 22: Results – Poisson

## Slide 23: Results – Poisson
Notes: Dropped further investigation of funcational approaches

## Slide 24: Results – Tri-dexel
32s
3.8M Δ
51s
3.0M Δ

## Slide 25: Results – Tri-dexel

## Slide 26: Conclusion
Direct intersection
  fails due to numeric issues
Ball pivoting algorithm
  looses concave features
  does not use normals
  may create holes or role inside
Poisson
  Fitting to imprecise in feature-rich regions
Tri-dexel
  feature reconstruction using normals
  long runtime
Notes: Finally, based on these results, the tri-dexel approach works best for extracting a triangulated surface from the VML
Will be subject to further research and development

## Slide 28: Additional slides

## Slide 29: Resolutions – BPA
50
100
200
400

## Slide 30: Resolutions – Poisson
50
100
200
400

## Slide 31: Resolutions – Tri-dexel
50
100
200
400

## Slide 32: Tri-dexel feature reconstruction

## Slide 33: Tri-dexel regularization

## Slide 34: Tri-dexel cell slicing